## Slide 1
SUBJECT NAME: Microprocessor
SUBJECT CODE: 303105210

## Slide 2
A microprocessor is a programmable electronics chip that has computing and decision making capabilities similar to central processing unit of a computer.
It is clock driven IC
It is Si type of semiconductor chip which contain no. of transistors.
It is register array based device.
Microprocessor is used as multipurpose
Microprocessor
I/P
O/P
What is Microprocessor?
Technology Used: The semiconductor manufacturing technologies used for chips are:
 Transistor-Transistor Logic (TTL)
 Emitter Coupled Logic (ECL)
 Complementary Metal-Oxide Semiconductor (CMOS)

## Slide 3
Classification of Microprocessors:
Based on size of data bus:
4-bit microprocessor
8-bit microprocessor
16-bit microprocessor
32-bit microprocessor
Based on application:
General-purpose microprocessor- used in general computer system and can be used by programmer for any application. Examples, 8085 to Intel Pentium.
Microcontroller- microprocessor with built-in memory and ports and can be programmed for any generic control application. Example, 8051.
Special-purpose processors- designed to handle special functions required for an application. Examples, digital signal processors and application-specific integrated circuit (ASIC) chips.
Based on architecture:
Reduced Instruction Set Computer (RISC) processors
Complex Instruction Set Computer (CISC) processors

## Slide 4
History of Microprocessors:

## Slide 5: 4-BIT MICROPROCESSORS
4

## Slide 6: INTEL 4004
Introduced in 1971.
It was the first microprocessor by Intel.
It was a 4-bit µP.
Its clock speed was 740KHz.
It had 2,300 transistors.
It could execute around 60,000 instructions per second.
5

## Slide 7: INTEL 4040
Introduced in 1974.
It was also 4-bit µP.
6

## Slide 8: 8-BIT MICROPROCESSORS
7

## Slide 9: INTEL 8008
Introduced in 1972.
It was first 8-bit µP.
Its clock speed was 500 KHz.
Could execute 50,000 instructions per second.
8

## Slide 10: INTEL 8080
Introduced in 1974.
It was also 8-bit µP.
Its clock speed was 2 MHz.
It had 6,000 transistors.
Was 10 times faster than
8008.
Could execute 5,00,000 instructions per second.
9

## Slide 11: INTEL 8085
Introduced in 1976.
It was also 8-bit µP.
Its clock speed was 3 MHz.
Its data bus is 8-bit and address bus is 16-bit.
It had 6,500 transistors.
Could execute 7,69,230 instructions per second.
It could access 64 KB of
memory.
It had 246 instructions.
10

## Slide 12: 16-BIT MICROPROCESSORS
11

## Slide 13: Introduced in 1978.
INTEL 8086
It was first 16-bit µP.
Its clock speed is 4.77 MHz, 8 MHz and 10 MHz, depending on the version.
Its data bus is 16-bit and address bus is 20-bit.
It had 29,000 transistors.
Could execute 2.5 million instructions per second.
It could access 1 MB of memory.
It had 22,000 instructions.
It had Multiply and Divide
instructions.
12

## Slide 14: INTEL 8088
Introduced in 1979.
It was also 16-bit µP.
It was created as a cheaper
version of Intel’s 8086.
It was a 16-bit processor with an 8-bit external bus.
13

## Slide 15: INTEL 80186 & 80188
Introduced in 1982.
They were 16-bit µPs.
Clock speed was 6 MHz.
14

## Slide 16: INTEL 80286
Introduced in 1982.
It was 16-bit µP.
Its clock speed was 8 MHz.
15

## Slide 17: 32-BIT MICROPROCESSORS
16

## Slide 18: Introduced in 1986.
INTEL 80386
It was first 32-bit µP.
Its data bus is 32-bit and address bus is 32-bit.
It could address 4 GB of memory.
17

## Slide 19: Introduced in 1989.
INTEL 80486
It was also 32-bit µP.
It had 1.2 million transistors.
Its clock speed varied from 16 MHz to 100 MHz depending upon the various versions.
18

## Slide 20: Introduced in 1993.
INTEL PENTIUM
It was also 32-bit µP.
It was originally named 80586.
Its clock speed was 66 MHz.
19

## Slide 21: INTEL PENTIUM PRO
Introduced in 1995.
It was also 32-bit µP.

## Slide 22: INTEL PENTIUM II
Introduced in 1997.
It was also 32-bit µP.
21

## Slide 23: INTEL PENTIUM II XEON
Introduced in 1998.
It was also 32-bit µP.
22

## Slide 24: INTEL PENTIUM III
Introduced in 1999.
It was also 32-bit µP.
23

## Slide 25: INTEL PENTIUM IV
Introduced in 2000.
It was also 32-bit µP.
24

## Slide 26: INTEL DUAL CORE
Introduced in 2006.
It is 32-bit or 64-bit µP.
It has two cores.
Both the cores have there own internal bus and L1 cache, but share the external bus and L2 cache
25

## Slide 27
26

## Slide 28: 64-BIT MICROPROCESSORS
27

## Slide 29: INTEL CORE 2
Introduced in 2006.
It is a 64-bit µP.
28

## Slide 30: INTEL CORE I7
Introduced in 2008.
It is a 64-bit µP.
29

## Slide 31: INTEL CORE I5
Introduced in 2009.
It is a 64-bit µP.
30

## Slide 32: INTEL CORE I3
Introduced in 2010.
It is a 64-bit µP.
31

## Slide 34
Formal structure of Microprocessors:

## Slide 35
Bit: A bit is a single binary digit.
Word: A word refers to the basic data size or bit size that can be processed by the arithmetic and logic unit of the processor. A 16-bit binary number is called a word in a 16-bit processor.
Bus: A bus is a group of wires/lines that carry similar information.
System Bus: The system bus is a group of wires/lines used for communication between the microprocessor and peripherals.
Memory Word: The number of bits that can be stored in a register or memory element is called a memory word.
Address Bus: It carries the address, which is a unique binary pattern used to identify a memory location or an I/O port. For example, an eight bit address bus has eight lines and thus it can address 28 = 256 different locations. The locations in hexadecimal format can be written as 00H – FFH.
Data Bus: The data bus is used to transfer data between memory and processor or between I/O device and processor. For example, an 8-bit processor will generally have an 8-bit data bus and a 16-bit processor will have 16-bit data bus.
Control Bus: The control bus carry control signals, which consists of signals for selection of memory or I/O device from the given address, direction of data transfer and synchronization of data transfer in case of slow devices.

## Slide 36
Each microprocessor has a set of instructions, a list which is provided by the microprocessor manufacturer. The instruction set of a microprocessor is provided in two forms: binary machine code and mnemonics.
Microprocessor communicates and operates in binary numbers 0 and 1. The set of instructions in the form of binary patterns is called a machine language
Language of Microprocessors:
and it is difficult for us to understand. Therefore, the binary patterns are given abbreviated names, called mnemonics, which forms the assembly language.
The conversion of assembly-level language into binary machine-level language is done by using an application called assembler.

## Slide 37
Microprocessors Vs Microcontroller:

## Slide 38
Microprocessors Vs Microcontroller:

## Slide 39
Application - <<Microprocessor>>

## Slide 41: THANK YOU