## Slide 1: Unit-9 Memory Organization
krunal.vyas@darshan.ac.in
9601901005
Computer Engineering Department
Prof. Krunal D. Vyas
Computer Organization & Architecture (COA)
GTU # 3140707

## Slide 2

Looping
Outline
  Memory Hierarchy
  Main Memory
  Auxiliary Memory
  Associative Memory
  Cache Memory
  Virtual Memory
  Questions asked in GTU exam

## Slide 3: Memory Hierarchy
Section - 1

## Slide 4: Memory Hierarchy
Magnetic
tapes
Magnetic
disks
I/O processor
Main
memory
Cache
memory
CPU

## Slide 5: Main Memory
Section - 2

## Slide 6: Random access memory (RAM)
Used in computers for the temporary storage of programs and data.
Read and write both operations are performed by RAM which requires fast cycle times as not to slow down the computer operation.
It is volatile and lose all stored information if power is interrupted or turned off.
RAMs typically come with word capacities of 1K, 4K, 8K, 16K, etc.. and word sizes of 1, 4 or 8-bits.
It can be expanded by combining several memory chips.

## Slide 7: SRAM v/s DRAM
Static RAM | Dynamic RAM
1. SRAM has lower access time, so it is faster compared to DRAM. | 1. DRAM has higher access time, so it is slower than SRAM.
2. SRAM is costlier than DRAM. | 2. DRAM costs less compared to SRAM.
3. SRAM requires constant power supply, which means this type of memory consumes more power. | 3. DRAM offers reduced power consumption, due to the fact that the information is stored in the capacitor.
4. Due to complex internal circuitry, less storage capacity is available compared to the same physical size of DRAM memory chip. | 4. Due to the small internal circuitry in the one-bit memory cell of DRAM, the large storage capacity is available.
5. SRAM has low packaging density. | 5. DRAM has high packaging density.
6. No need to refresh periodically. | 6. Due to capacitor used as storage element, information may lose over period of time. So, need to refresh periodically.
7. Uses an array of 6 transistors for each memory cell. | 7. Uses a single transistor and capacitor for each memory cell.

## Slide 8: Read-Only Memory (ROM)
A read-only memory (ROM) is essentially a memory device in which permanent binary information is stored.
The binary information must be specified by the designer and is then embedded in the unit to form the required interconnection pattern.
Once the pattern is established, it stays within the unit when the power is turned off and on again.
A ROM which can be programmed is called a PROM. The process of entering information in a ROM is known as programming.
ROMs are used to store information which is of fixed type, such as tables for various functions, fixed data and instructions.
ROMs can be used for designing combinational logic circuits.

## Slide 9: Memory Address Map
Example:- Show how to combine several 1K x 8 PROMs to produce 4K x 8 PROM.
Solution:- 1K x 8 PROM has 10 number of address lines because 210 = 1024 (1K).
We need total 4 number of 1K x 8 PROM chips to make one 4K x 8 PROM chip.
PROM 1
1K x 8
PROM 1
1K x 8
PROM 1
1K x 8
PROM 1
1K x 8
D7
D0
A9
A0
A10
A11
2 to 4 decoder
O0
O1
O2
O3

## Slide 10: Memory Address Map
A11
A10
A9
A8
A7
A6
A5
A4
A3
A2
A1
A0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
1
1
Memory chip | Starting address | Ending address
PROM 1 | 000 H | 3FF H
PROM 2 | 400 H | 7FF H
PROM 3 | 800 H | BFF H
PROM 4 | C00 H | FFF H

## Slide 11: Auxiliary Memory
Section - 3

## Slide 12: Magnetic Disks
Tracks
Read/write head
Sector
Circular plate of metal or plastic coated with magnetized material.
Often both sides of the disk are used and several disks may be stacked on one spindle with read/write heads available on each surface.
All disks rotate together at high speed and are not stopped or started for access purposes.
Bits are stored in the magnetized surface in spots along concentric circles called track.
The tracks are commonly divided into sections called sectors.

## Slide 13: Magnetic Tape
Magnetic tape transport consists of the electrical, mechanical and electronic components to provide the parts and control mechanism for a magnetic-tape unit.
The tape itself is a strip of plastic coated with a magnetic recording medium.
Bits are recorded as magnetic spots on the tape along several tracks.
Magnetic tape units can be stopped, started to move forward or in reverse, or can be rewound. However, they cannot be started or stopped fast enough between individual characters.
A tape unit is addressed by specifying the record number and the number of characters in the record.

## Slide 14: Associative Memory
Section - 4

## Slide 15: Associative Memory(Content Addressable Memory)
The time required to find an item stored in memory can be reduced considerably if stored data can be identified for access by the content of the data itself rather than by an address.
A memory unit accessed by content is called an associative memory or content addressable memory (CAM).
This type of memory is accessed simultaneously and in parallel on the basis of data content rather than by specific address or location.
Argument register (A)
Key register (K)
Associative memory
array and logic
m words
n bits per word
M
Match
register
Output
Input
Read
Write
101 111100
111 000000
100 111100
101 000001
A
K
W1
W2
No match
Match
100 111100
101 000001

## Slide 16: Associative Memory
A1
Aj
An
K1
Kj
Kn
C11
C1j
C1n
Ci1
Cij
Cin
Cm1
Cmj
Cmn
M1
Mi
Mm
Word 1
Word i
Word m
Bit 1
Bit j
Bit n

## Slide 17: Cache Memory
Section - 5

## Slide 18: Cache Memory
Cache is a fast small capacity memory that should hold those information which are most likely to be accessed.
The basic operation of the cache is, when the CPU needs to access memory, the cache is examined.
If the word is found in the cache, it is read from the fast memory. If the word addressed by the CPU is not found in the cache, the main memory is accessed to read the word.
The transformation of data from main memory to cache memory is referred to as a mapping process.
The performance of the cache memory is frequently measured in terms of a quantity called hit ratio.
When the CPU refers to memory and finds the word in cache, it is said to produce a hit.
If the word is not found in cache, it is in main memory and it counts as a miss.
The ratio of the number of hits divided by the total CPU references to memory (hits plus misses) is the hit ratio.
Hit ratios of 0.9 and higher have been reported.

## Slide 19: Associative Mapping
Argument register
0 1 0 0 0
3 4 5 0
0 2 7 7 7
6 7 1 0
2 2 3 4 5
1 2 3 4
CPU address (15 bits)
Address
Data

## Slide 20: Direct Mapping
32K X 12
Main memory
Address = 15 bits
Data = 12 bits
512 X 12
Cache memory
Address = 9 bits
Data = 12 bits
000
777
000
777
00
77
Octal
address
Octal
address
Tag
Index
6 bits
9 bits

## Slide 21: Direct Mapping
1 2 2 0
2 3 4 0
3 4 5 0
4 5 6 0
5 6 7 0
6 7 1 0
00000
00777
01000
01777
02000
02777
Memory data
Memory address
Main Memory
1 2 2 0
6 7 1 0
0 0
0 2
000
777
Cache Memory
Tag
Data
Index address

## Slide 22: Set-Associative Mapping
3 4 5 0
6 7 1 0
0 1
0 2
000
777
Tag
Data
Index
5 6 7 0
2 3 4 0
0 2
0 0
Tag
Data

## Slide 23: Virtual Memory
Section - 6

## Slide 24: Virtual Memory
Virtual memory is used to give programmers the illusion that they have a very large memory at their disposal, even though the computer actually has a relatively small main memory.
A virtual memory system provides a mechanism for translating program-generated addresses into correct main memory locations.
Address space
An address used by a programmer will be called a virtual address, and the set of such addresses is known as address space.
Memory space
An address in main memory is called a location or physical address. The set of such locations is called the memory space.

## Slide 25: Virtual Memory
Relation between Address space & Memory space
Program 1
Data 1,1
Data 1,2
Program 2
Data 2,1
Program 1
Data 1,1
Address Space
Memory Space
N = 1024K = 220
M = 32K = 215
Auxiliary Memory
Main Memory

## Slide 26: Virtual Memory
Virtual address register (20 bits)
Memory mapping table
Memory table buffer register
Main memory address register (15 bits)
Main memory
Main memory buffer register
Virtual Address

## Slide 27: Questions asked in GTU exam
Section - 7

## Slide 28: Questions asked in GTU exam
For cache memories explain:
  Direct Mapping algorithm
  Set Associative Mapping
  Associative Mapping
What is virtual memory? Explain relation between address space and memory space in virtual memory system.
How main memory is useful in computer system? Explain the memory address map of RAM and ROM.
Write a short note on associative memory.
Content Addressable Memory.
Compare SRAM and DRAM.
Explain what do you understand by Cache memories
What is cache miss and cache hit?
Define hit ratio.